Payload Title:	OSIRIS LITE

Payload Class:		Small		Large 		(circle one)

Payload ID:	03

Institution:	The Pennsylvania State University

Contact Name:	Dr. Sven Bilén, Allen Kummer

Contact Phone:	814-863-1526, 215-622-8230

Contact E-mail:	sbilen@engr.psu.edu, atk5025@psu.edu

Submit Date:	6/1/2011

- Mechanical Specifications:

  - Measured weight of the payload (not including payload plate)

| Subsystem | Mass (g) | Quantity | Total Mass (g) |
| --- | --- | --- | --- |
| PWR EXP | 124.85 | 1 | 124.85 |
| GNC | 87.54 | 1 | 87.54 |
| PWR SUB | 85.83 | 1 | 85.83 |
| CDH | 89.98 | 1 | 89.98 |
| PWR Distro | 5.32 | 6 | 31.92 |
| solar panel | 95.56 | 1 | 95.56 |
| back plane board | 96.67 | 1 | 96.67 |
| sun sensors | 9.28 | 5 | 46.4 |
| Skeleton w/ negZ Panel | 521.01 | 1 | 521.01 |
| Side Skin Panels | 352.37 | 1 | 352.37 |
| posZ Skin Panel w/ Standoffs | 72.93 | 1 | 72.93 |
| Skin Fasteners (20) | 7.14 | 1 | 7.14 |
| Board Bracket | 7.87 | 5 | 39.35 |
| sun sensor box | 11.55 | 5 | 57.75 |
|  |  | Total Mass | 1709.3 |

Current payload mass is 2377.3 g with all masses measured.

  - Provide a mechanical drawing detailing the major components of your payload and specifically how your payload is attached to the payload mounting plate.

See attached PDF drawings.

  - If you are flying anything that is potentially hazardous to HASP or the ground crew before or after launch, please supply all documentation provided with the hazardous components (i.e. pressurized containers, radioactive material, projectiles, rockets…)

The OLite bus does not contain any potentially hazardous components.

  - Other relevant mechanical information

Sun sensor boxes, shown in orange on provided drawings, exceed the width of the specified payload footprint. These boxes are 29.8cm (11.7in) above the interface plate and will not cause mechanical interference.

- Power Specifications:

  - Payload power specification

OLite will draw power through out the flight as described in the table below

| GNC Experiment | 0.25 | W |
| --- | --- | --- |
| PWR Experiment | 0.33 | W |
| CDH Subsystem | 1.75 | W |
| Housekeeping | 0.5 | W |
| Thermal | 2 | W |
| Total | 4.83 | W |
| PWR Efficiency | 75% |  |
| Total | 6.0375 | W |
| Margin | 8.9625 | W |

Simplified Schematic of OLite Power Systems

- Downlink Telemetry Specifications:

  - Serial data downlink format: 	Stream		Packetized	(circle one)

  - Approximate serial downlink rate (in bits per second)

961 bps

  - Specify your serial data record including record length and information contained in each record byte.

| Event Packet |
| --- |
| Data type | Size in bits | Descr |
| Subframe ID | 8 | 0, 1, 2, 3… 255, 0, 1, 2… |
| Time Stamp | 32 | UNIX time |
| Frame ID | 8 | E |
| Packet Size | 32 | Size of the entire packet |
| Packet Data | 56 | Operating system and flight software event reports |
| IRIG Standard Sync Word | 16 | 0xEB90 |
| Total Size: | 152 bits | 19 bytes |
| Frequency | 1 Hz | Once every second (on average) |

| Channel Packet |
| --- |
| Data type | Size in bits | Descr |
| Subframe ID | 8 | 0, 1, 2, 3… 255, 0, 1, 2… |
| Time Stamp | 32 | UNIX time |
| Frame ID | 8 | C |
| Packet Size | 32 | Size of the entire packet |
| Packet Data | 640 | Housekeeping data and debugging information |
| IRIG Standard Sync Word | 16 | 0xEB90 |
| Total Size: | 736 bits | 92 bytes |
| Frequency | 1 Hz | Once every second |

| Data Product Packet |
| --- |
| Data type | Size in bits | Descr |
| Subframe ID | 8 | 0, 1, 2, 3… 255, 0, 1, 2… |
| Time Stamp | 32 | UNIX time |
| Frame ID | 8 | D |
| Packet Size | 32 | Size of the entire packet |
| Packet Data | 640 (average) | Raw instrument data |
| IRIG Standard Sync Word | 16 | 0xEB90 |
| Total Size: | 736 bits | 92 bytes |
| Frequency | 0.1 Hz | Once every 10 seconds |

- Number of analog channels being used:

2 analog lines are being used

- If analog channels are being used, what are they being used for?

Analog 1 (Pin K) Command and Data Handling Current and Analog 2 (Pin M) Voltage Sensors

- Number of discrete lines being used:

No discrete lines are being used.

- If discrete lines are being used what are they being used for?

N/A

- Are there any on-board transmitters?  If so, list the frequencies being used and the transmitted power.

No

- Other relevant downlink telemetry information.

N/A

- Uplink Commanding Specifications:

  - Command uplink capability required:	Yes	No 	(circle one)

  - If so, will commands be uplinked in regular intervals:	Yes	No	(circle one)

  - How many commands do you expect to uplink during the flight (can be an absolute number or a rate, i.e. n commands per hour)

If everything operates correctly we expect to send no (0) uplink commands.

  - Provide a table of all of the commands that you will be uplinking to your payload

| Command Packet Organization |
| --- |
| Data type | Size in bits | Descriptions |
| Module ID | 5 | Module IDs listed in Table 1. |
| Command ID | 5 | Command IDs listed in Table 2. |
| Command Arguments | 4 | Command arguments listed under each commands in Table 2. |
| CRC Checksum | 2 | 2 bit CRC checksum calculated with command. |

Table 1: Module IDs

| Module | Opcode |
| --- | --- |
| ADC | 0C |
| CAM | 01 |
| CMD | 0E |
| COM | 00 |
| DISTRO | 02 |
| DP | 0F |
| GPS | 0B |
| HEATER | 03 |
| MAG | 06 |
| MPPT | 0A |
| MUX | 09 |
| PARAM | 10 |
| PROC | 07 |
| SCM | 0D |
| TIME | 04 |
| WDT | 08 |
| ZMOD | 05 |

Table 2: Command IDs, sorted by modules alphabetically

#### [00] CMD_ADC_INIT

Module: ADC

Description: Initialize all ADCs

##### Arguments

#### [01] CMD_ADC_KILL

Module: ADC

Description: Kill ADC process

##### Arguments

#### [02] CMD_ADC_INTERNAL_READ

Module: ADC

Description: Read data from internal ADCs and push to channel. Argument 1 of the command is the internal ADC channel

##### Arguments

[Enum] Channel

ADC0

ADC1

#### [03] CMD_ADC_EXTERNAL_READ

Module: ADC

Description: Read from external ADC and store the value in the channel. Argument is 0 or 1 to determine which ADC chip to read from.

##### Arguments

[Enum] Chip

CHIP_A

CHIP_B

#### [00] CMD_CMD_SPAWN

Module: CMD

Description: Spawn the specified module ID provided by argument 0. Module ID should be an integer.

##### Arguments

[Int ] Module ID

Min:

Max: 255

#### [00] CMD_DISTRO_INIT

Module: DISTRO

Description: Initialize distro module.

##### Arguments

#### [01] CMD_DISTRO_KILL

Module: DISTRO

Description: Kill distro module.

##### Arguments

#### [02] CMD_DISTRO_COM_3

Module: DISTRO

Description: Set power state (ON/OFF) for 3V com.

##### Arguments

[Enum] new_state

UNKNOWN

ON

OFF

#### [03] CMD_DISTRO_COM_5

Module: DISTRO

Description: Set power state (ON/OFF) for 5V com.

##### Arguments

[Enum] new_state

UNKNOWN

ON

OFF

#### [04] CMD_DISTRO_PWR

Module: DISTRO

Description: Set power state (ON/OFF) for power experiment.

##### Arguments

[Enum] new_state

UNKNOWN

ON

OFF

#### [00] CMD_DP_INIT

Module: DP

Description: Initialize data product.

##### Arguments

#### [01] CMD_DP_KILL

Module: DP

Description: Terminate data product.

##### Arguments

#### [00] CMD_HEATER_INIT

Module: HEATER

Description: Initialize heater.

##### Arguments

#### [01] CMD_HEATER_KILL

Module: HEATER

Description: Kill heater.

##### Arguments

#### [02] CMD_HEATER_POWER

Module: HEATER

Description: Set heater to power state (ON/OFF) specified by Arg 1.

##### Arguments

[Enum] power_state

ON

OFF

#### [00] CMD_MAG_INIT

Module: MAG

Description: Initialize the magnetometer: continuous measuring mode, high gain sensitivity, 10hz frequency, no bias.

##### Arguments

#### [01] CMD_MAG_KILL

Module: MAG

Description: Kill the magnetometer.

##### Arguments

#### [02] CMD_MAG_RESET

Module: MAG

Description: Reset magnetometer to initial settings: continuous measuring mode, high gain sensitivity, 10hz frequency, no bias.

##### Arguments

#### [03] CMD_MAG_MODE

Module: MAG

Description: Change mode of magnetometer to mode specified by CMD_MAG_MODE_args.

##### Arguments

[Enum] cmd_args

IDLE

CONTINUOUS

SINGLE

#### [04] CMD_MAG_SELF_TEST

Module: MAG

Description: Enter self test mode, acquire and report test data, and restore prior mode.

##### Arguments

#### [05] CMD_MAG_GET_X

Module: MAG

Description: Get X vector.

##### Arguments

#### [06] CMD_MAG_GET_Y

Module: MAG

Description: Get y vector.

##### Arguments

#### [07] CMD_MAG_GET_Z

Module: MAG

Description: Get z vector.

##### Arguments

#### [08] CMD_MAG_GET_DATA

Module: MAG

Description: Get x, y, and z vectors.

##### Arguments

#### [00] MPPT_TEST_ROB

Module: MPPT

Description: Rob's test command for a test module

##### Arguments

#### [00] CMD_MUX_INIT

Module: MUX

Description: Initializes mux, setting up or joining with semaphore.

##### Arguments

#### [01] CMD_MUX_KILL

Module: MUX

Description: Kills mux, closing and attempting to destroy semaphore.

##### Arguments

#### [02] CMD_MUX_SET_CHANNEL

Module: MUX

Description: Sets mux to specified channel (ranging from 0 to 31)

##### Arguments

[Int ] channel

Min:

Max: 31

#### [00] CMD_PARAM_INIT

Module: PARAM

Description: Initialized param module.

##### Arguments

#### [01] CMD_PARAM_KILL

Module: PARAM

Description: Terminate param module.

##### Arguments

#### [00] CMD_PROC_INIT

Module: PROC

Description: Initializes proc resources

##### Arguments

#### [01] CMD_PROC_KILL

Module: PROC

Description: Unallocates resources from proc to kill it

##### Arguments

#### [02] CMD_PROC_DOWNLINK

Module: PROC

Description: Pushes data to channel for downlink

##### Arguments

#### [03] PROC_MEM_USED

Module: PROC

Description: Retrieves current amount of memory in use

##### Arguments

#### [04] CMD_MEM_FREE

Module: PROC

Description: Retrieves current free memory

##### Arguments

#### [05] CMD_MEM_TOTAL

Module: PROC

Description: Retrieves total memory

##### Arguments

#### [06] CMD_PROC_CPU_USE

Module: PROC

Description: Retrieves current percentage of CPU usage

##### Arguments

#### [07] CMD_PROC_RUNNING

Module: PROC

Description: Retrives current number of processes in 'Running' state

##### Arguments

#### [08] CMD_PROC_SLEEPING

Module: PROC

Description: Retrieves current number of processes in 'Sleeping' state

##### Arguments

#### [09] CMD_PROC_STOPPED

Module: PROC

Description: Retrieves current number of processes in 'Stopped' state

##### Arguments

#### [10] CMD_PROC_ZOMBIE

Module: PROC

Description: Retrieves number of processes in 'Zombie' state

##### Arguments

#### [11] CMD_PROC_TOTAL_PS

Module: PROC

Description: Retrieves current number of total processes

##### Arguments

#### [00] CMD_TIME_REMOVE

Module: TIME

Description: Remove all time requests for specified module.

##### Arguments

[Enum] module_id

COM

CAM

HEATER

TIME

ZMOD

DISTRO

MAG

PROC

WDT

#### [01] CMD_TIME_REMOVE_ALL

Module: TIME

Description: Remove all time requests.

##### Arguments

#### [02] CMD_TIME_INTERVAL

Module: TIME

Description: Change timer interval to specified value. Arg 1 is number of seconds, Arg 2 is number of nanoseconds.

##### Arguments

[Int ] sec

Min:

Max:

[Int ] nsec

Min:

Max:

#### [00] CMD_WDT_INIT

Module: WDT

Description: Initialize watchdog

##### Arguments

#### [01] CMD_WDT_TOGGLE_LIGHT

Module: WDT

Description: Toggle watchdog LED on/off.

##### Arguments

#### [02] CMD_WDT_KICK

Module: WDT

Description: Kick file. If this is not done soon enough the system restarts.

##### Arguments

#### [03] CMD_WDT_RESTART

Module: WDT

Description: Overflow the watchdog and reset the entire system

##### Arguments

#### [04] CMD_WDT_KILL

Module: WDT

Description: Kill the WDT module

##### Arguments

  - Are there any on-board receivers?  If so, list the frequencies being used.

No

  - Other relevant uplink commanding information.

N/A

- Integration and Logistics

  - Date and Time of your arrival for integration:

Sunday afternoon July 31st

  - Approximate amount of time required for integration:

8 Hours

  - Name of the integration team leader:

Allen Kummer

  - Email address of the integration team leader:

Atk5025@psu.edu

  - List ALL integration participants (first and last names) who will be present for integration with their email addresses:

Allen Kummer atk5025@psu.edu

Sven Bilén sbilen@engr.psu.edu

Andre Coleman avc5184@psu.edu

Daniel Gilbert dbg5062@psu.edu

Thomas Connors tmc5186@psu.edu

  - Define a successful integration of your payload:

A successful integration will demonstrate that the payload passes:

1) a mechanical fit check,

2) electrical interfaces (power draw, EMI, pinouts),

3) successfully execute uplink commands from the HASP gondola,

4) successfully downlink data through the HASP gondola,

5) successfully operate during environmental test.

  - List all expected integration steps:

- Mechanical mount OLite to HASP Gondola

- Connect HASP power cable

- Verify power connection through communications test with our own laptop

- Connect HASP communications cable

- Send command from HASP to OLite and verify reception and proper execution

- Send data from OLite through HASP downlink interface

- While other payload radios are operating, verify that communications can be maintained

  - List all checks that will determine a successful integration:

- Mechanical Check

- Verify payload current draw powers up while communicating with PSU computers

- Verify that OLite 2 communicates properly with the HASP gondola. Verify Uplink and downlink capabilities

- Verify operation through thermal vacuum checkout

  - List any additional LSU personnel support needed for a successful integration other than directly related to the HASP integration (i.e. lifting, moving equipment, hotel information/arrangements, any special delivery needs…):

N/A

  - List any LSU supplied equipment that may be needed for a successful integration:

Adjustable power supply (or supplies) that can provide output voltages: 3V, 5V, and 30V. Oscilloscope (preferably mixed signal that can serve as logic analyzer). Soldering station for last minute harness modifications. If these cannot be provided, the OLite 2 team can bring them along.