## Slide 1: Introduction to Electronics
LaACES, Lecture 02.01
Notes: Prepared by Jim Giammanco
<giamman@rouge.phys.lsu.edu>

## Slide 2
What should you already know?
  Definitions of electrical quantities
    Electric potential (volts, millivolts, microvolts)
    Electric current (amperes, milliamps, microamps)
    Electrical resistance (ohms, kilo-ohms, mega-ohms)
    Electric power (watts, kilowatts, milliwatts
  Ohms Law and power relationships
    For DC circuits
    For AC circuits

## Slide 3: Electric Potential
1 volt = 1 joule of energy per coulomb of charge
Some examples:
flashlight battery – 1.5 V (DC)
car battery – 12 V (DC)
wall socket – 120 V (AC)
overhead power lines – 6,000 to 250,000 V (AC)

## Slide 4: Electric Current
1 ampere = movement of 1 coulomb of charge per time interval of 1 second
Some examples:
Flashlight – 300 milliamps (DC)
Toaster – 10 amperes (AC)
Automobile starter – 150 amperes (DC)
Quartz wristwatch – a few microamps (10-6 ampere)
Enough to “shock” – a few milliamps (10-3 ampere)

## Slide 5: Electric Resistance
1 ohm (Ω) of resistance allows a potential of 1 volt to cause a current of 1 ampere to flow in a circuit
Ohms’s Law V = I R
V = potential in volts
I = current in amperes
R = resistance in oms

## Slide 6: Electric Power
1 watt of power is produced when a potential of 1 volt causes a current of 1 ampere to flow in a circuit
P = I V
V = potential in volts
I = current in amperes
R = resistance in ohms
P = power in watts
Using Ohm’s Law and P = I V, then P = I2 R = V2 / R

## Slide 7: Electric Power
Some examples…
Quartz wristwatch – 0.000001 watt (1 microwatt)
Flashlight – 1 watt
Balloon radio beacon – 5 watts
Table lamp – 60 watts
27” television set – 130 watts
Hair dryer – 1100 watts
Clothes dryer – 5000 watts (5 kilowatts)
State of Louisiana – 8,000,000,000 watts (8000 megawatts)

## Slide 8: How To Use a Digital Multimeter
Digital MultiMeter (DMM)
Measures voltage, current, resistance,
sometimes other parameters
This one cost less than $5
AC and DC voltage
DC current
Resistance
Diode and Transistor properties
Battery tester

## Slide 9
BLACK test lead is plugged
Into the COM (common)
terminal
RED test lead is plugged
Into the VΩmA terminal
terminal
Select the proper RANGE
Some $$ DMMs are autoranging
For large DC currents
(up to 10 amperes)
RED test lead is connected
To the 10ADC terminal
Taking Measurements

## Slide 10
Voltage measurements require the DMM to be
connected in parallel (i.e., across) the circuit element
whose voltage is being measured
Here’s a simple battery
and lamp circuit
Let’s measure the voltage
across the lamp

## Slide 11
To measure current, the DMM
must be connected in series
(i.e., in line with) the circuit
element whose current is being
measured

## Slide 12
Here’s how to
measure the
resistance of an
element
Note: the element
is removed from
its circuit
The RANGE is 0-2000 Ω
So the reading is interpreted as
976 Ω, or 0.976 K Ω

## Slide 13
*****WARNING*****
Don’t try this at home.
We are what you call “experts”
What happens if you connect a DMM,
set to read current,in parallel with a
voltage source, such as a battery?
Some of the magic smoke may
Escape from your DMM.
Fortunately, even this inexpensive
DMM includes a protective fuse.
So your DMM might not be destroyed.

## Slide 14: Activity A02.01
Practice making measurements with a digital multimeter. Without blowing any fuses!
Practice calculating resistance and power using Ohm’s Law and the power relation.