## Slide 1: Schematics, Prototyping and Soldering Lecture

## Slide 2: Schematic Diagrams
Schematic diagrams represent an electronic circuit in symbolic form.
A schematic need not depict the actual physical arrangement of the components

## Slide 3: SkeeterSat Schematic

## Slide 4: Schematic Symbols Cont.
Wires and wire connections
Current practice:
Either A or B is acceptable C is the preferred style
D is seldom used E is interpreted as a non-connection

## Slide 5: Schematic Symbols Cont.
Power sources (V) common connections (GND)
The “+” sign may not always appear on a battery symbol. By convention, the longer horizontal line represents the positive terminal
Note that no polarity is shown for the ac source

## Slide 6: Schematic Symbols Cont.
Common connections (GND)
“Earth” means an actual connection to a conductor driven into the soil.
“Chassis” means a bonded electrical connection to the metallic case of chassis of a device.

## Slide 7: Schematic Symbols Cont.
Resistors (R) and Capacitors (C)

## Slide 8: Schematic Symbols
Inductors (L) and Transformers (T)
simple
inductors
transformers
The two parallel lines indicate that the inductor is wound on a core of iron, iron powder, or ferrite material.
adjustable
adjustable
tapped

## Slide 9: Schematic Symbols
Diodes (D)
The arrow points in the allowed direction of
conventional (positive charges) current flow.
The bar represents the cathode, marked with a band on most parts.

## Slide 10: Schematic Symbols
Transistors (Q)
bipolar NPN
junction transistor
bipolar PNP
junction transistor
N-channel junction
field-effect transistor
P-channel junction
field-effect transistor
N-channel MOS
field-effect transistor
P-channel MOS
field-effect transistor

## Slide 11: Schematic Symbols
Integrated circuits (U)
Most complex integrated circuits are represented on schematic diagrams as a rectangular block symbol, with pin numbers and, usually, pin functions indicated; but many logic integrated circuits have special symbols that identify their function.

## Slide 12: Schematic Symbols
Switches (S) and Relays (K)
single pole single throw
SPST
single pole double throw
SPDT
double pole single throw
DPST
double pole double throw
DPDT
rotary switch
1 pole, 5 position
single pole double throw
relay

## Slide 13: Drawing Schematic Diagrams
You can use one of the many schematic capture programs available on the internet for free. The SkeeterSat schematic shown earlier was prepared with ExpressPCB.
Schematic Capture Programs
ExpressPCB http://www.expresspcb.com/
Eagle http://www.cadsoftusa.com/freeware.htm
Schematic capture is a step in the design cycle where the electronic diagram of the electronic circuit is created by a designer.

## Slide 14: Building a prototype
Solderless breadboards
Perfboards or Protoboards
Manhattan Construction
Dead Bug Construction
Etched Circuit Boards

## Slide 15: Solderless Breadboards
The term breadboard originated in the early days of radio, when many experimenters actually built circuits on the wooden boards used in their mother’s kitchen for rolling out bread dough.
Modern solderless breadboards
Best thing to come along since sliced bread!
A ham radio transmitter circa 1930
Notes: Connections are made by plugging short pieces of solid (not stranded) hookup wire into the socket holes on the breadboard.
Solderless breadboards are not recommended for circuits operating at frequencies above couple of MHz or so

## Slide 16: Perfbord or Protoboard
Components are soldered to the board, with connections made using a combination of short pieces of wire and the copper traces already present on some versions of these boards.

## Slide 17: Manhattan Construction
Manhattan Style uses little “islands” of PCB material glues to a substrate s ties points for components.

## Slide 18: Dead Bug Construction
“Dead bug” style is a type of board design with the integrated circuits (IC’s) flipped upside-down with their pins sticking up into the air like a dead insect. While it is messy-looking, it can be used to make more compact circuits than other methods.

## Slide 19: Etched Circuit Boards
While etched boards are the most reliable method of circuit construction, they can be expensive in small quantities ($300+ per board). Cost per board drops rapidly when quantities exceed 25 or so.

## Slide 20: Prototyping with Surface Mounted Device (SMD) components
  Difficult to prototype SMD components without a PCB board
  Can solder wires directly to the leads
    -However, this requires a fair amount of precision and handling to accomplish. May unintentionally damage component if mishandled
    -Some devices are sensitive to electrostatic discharge (ESD) and can be destroyed by touching them.

## Slide 21: Breakout Boards
Common method for testing specific chips is to make or buy a board that draws out all the desired leads to terminals that are easier to interface with.

## Slide 22: Two-terminal SMD
  Resistors and Capacitors
    Case Code usually reported in XXYY format where XX is the length and YY in the width in mm or inches
    VERY important not to mix up imperial and metric values! Ex. 0603 can be 0.6mm x 0.3 mm OR 0.06 x 0.03 in
  Other two terminal devices such as LEDs have their own package sizes and dimensions
  Dimensions are always listed on the DATASHEET

## Slide 23: Multi-terminal SMD
  Wide variety of packages and footprints available
  Many manufacturers will adhere to standard package sizes common throughout the industry
      This is not true for all components
  Types of SMD footprints
      Small outline transistors (SOT), Small outline integrated circuit (SOIC), Dual Flat No-Lead (DFN), Ball Grid Array (BGA)

## Slide 24: Soldering Tutorial
Soldering – fastening metal objects together using molten metal (solder) as the glue.
Three requirements
Low melting point metal (wire solder)
Heat source (soldering iron)
Flux (to prevent surfaces from oxidizing)

## Slide 25: Types of Solder
Tin-Lead solders
60% Tin, 40% Lead - solid at 361° F, liquid at 374° F
63% Tin, 37% Lead - eutectic point is 361° F
no “pasty” range so joint movement less a problem
Silver-bearing Solder
62% Tin, 36% Lead, 2 % Silver - solid at 354 ° F,
liquid at 372 F
often used for surface mount components whose
contacts contain trace amounts of silver
Notes: .

## Slide 26: Soldering Irons
Constant wattage
Iron is continuously “ON” and eventually reaches equilibrium temperature
20 to 25 watt iron sufficient for circuit board assembly
Constant temperature
Tip incorporates a thermostatic element to maintain desired tip temperature
650 – 750 ° F appropriate for circuit board assembly
But wait…..even better…
Weller® 30 watt iron

## Slide 27: Soldering Irons
Temperature Controlled Solder Station
Feedback control maintains tip at desired temperature
Adjustable, often with analog or digital temperature display
Many have grounded tip to help prevent ESD damage
Weller® solder station

## Slide 28: Types of Flux
Rosin Flux
Type R – ordinary rosin – most common
Leaves a residue that can be removed for cosmetic reasons if desired.
Type RMA – mildly activated rosin
Type RA – activated rosin – use with care
RMA and RA fluxes leave a slightly corrosive residue that generally should be removed (with a solvent) after soldering
Acid Flux – NEVER, EVER use this for electronics

## Slide 29: Flux-core solder
Most solder used for electronics assembly is in wire form, with the flux incorporated inside the solder.
Multi-core solder has several (usually five) separate flux channels within the solder.
For circuit board assembly use wire solder with a diameter of about 0.025 inch or less

## Slide 30: Two Types of Soldering
1st type: Through Hole
  Component has metal leads that goes through the board.

## Slide 31: Two Types of Soldering
2nd type: Surface Mount.
  Component has metal pads that rest on top of board.

## Slide 32: Activities
A03.01 Use the supplied assortment of components and practice soldering them to the perfboard.
Notes: Click on the Activity link to access the instructions document for the activity.