## Slide 1: Basic Digital I/O

## Slide 2: Digital vs Analog Signal
Analog Signal
Digital Signal
I/O stands for “input & output,” This is how we will communicate information to and from the microcontroller
Digital means that it comes in a discrete set of possible values
  For the Arduino (and most microcontrollers), these are 0 and 1
This is opposed to an analog signal, which can take any possible value with in some range
IF you look at a signal as it varies with time
  Analog will be a smooth continuous wave
  Digital will be a series of square pulses with sharp, sudden changes

## Slide 3: Characteristics of a Digital Signal
To use digital signals as input or output we need to specify some details
How is the signal being transmitted?
  What is a physical connection?
  Is it a voltage, current, infrared light?
What defines 1 and what is a 0?
  These are logic levels, for the Arduino these are based on voltage
What do the 1s and 0s mean
  For anything other than a single, simple On/Off you need to define some kind of communication protocol

## Slide 4: Logic Levels Defining 0 and 1
The manufacturer of a digital device will give a set of specifications that define the voltages for High(0) and Low (0)
These are called the “Logic Levels”
  When discussing, you will often see terms like 5V TTL or 3.3V CMOS
  This is the underlying technology (ex., TTL - Transistor to Transistor Logic) and nominal voltage level
Devices will further group devices into “Logic Families” that share logic levels and additional specs
  For example, HCT uses the TTL levels but has additional high-speed capabilities
5V TTL and CMOS Logic levels for TI Devices
https://www.ti.com/lit/sg/sdyu001ab/sdyu001ab.pdf?ts=1758714419432
Notes: Fun, Spark. “Logi

## Slide 5: Logic Levels Output
VOH (Voltage Output High) - Minimum voltage that will be seen when the output is high
  So a digital 1 output will be between VOH and Vcc
VOL (Voltage Output Low) - Maximum voltage that will be seen when the output is low
  So a digital 0 output will be between 0 and VOL

## Slide 6: Logic Levels Input
VIH (Voltage Input High) - Minimum voltage that will be considered high
  Any voltage between VIH and Vcc will be read as a 1
VIL (Voltage Input Low) - Maximum voltage that will be considered a low
  Any voltage between 0 and VIL will be read as a 0

## Slide 7: Intermediate Region
Notice the gap between VIH and VIL? Because of this gap, there is a sharp distinction between 0 and 1
This makes digital signals less susceptible to errors caused by “background noise,” which would normally affect an analog signal
Also notice the outputs are more restricted than the inputs, this allows for slight voltage drop or rise between the output and input

## Slide 8: Mismatched logic levels
Look more closely at the two levels to the right
  Consider TTL output to CMOS input
  The TTL High output could be 3.0V (>2.4V), but this will fall in the intermediate range for CMOS input (<3.5V)
  So even though both are “5V Logic,” they may fail to work together
This mismatch is even worse with differing voltage levels, ie. 3.3V and 5V
  Devices called level shifters are used between the different logic levels

## Slide 9: Unipolar Digital Signals
The voltage levels we just looked at are examples of unipolar signals
In unipolar, low is assigned to 0 voltage, a.k.a ground. The high is assigned to the output voltage
The idle state (when not actively transmitting) can either be High or Low

## Slide 10: Bipolar Digital Signals
In some cases, you will see both positive and negative voltages used for a signal, called bipolar
The signal may or may not return to 0V when idle

## Slide 11: Single Ended Vs Differential
Signal can use a single wire and be measured compared to the device’s 0V (GND)
  This is called Singled Ended
  This requires a common ground between the transmitting device and the receiving device
An alternative is to use two lines and measure the difference
  The signal is split and transmitted with opposite polarity, giving x2 the effective signal when received
Differential Signal
Single Ended Signal

## Slide 12: Arduino Digital Signals
The Mega2560 Digital IOs have these characteristics
  Voltage Signals
  Unipolar
  Single Ended
  5V TTL Logic

## Slide 13: Digital Pins
Except for the power pins, all of the pins on the Arduino headers can be used for basic digital input output
Some of the pins have additional special functionality we will cover in later lectures
  Pins A0-A15 can be used for analog input
  Pins 0-1, 14-19 are for Serial Communication
  Pins 20-21 I2C Communication
  Pins 50-53 SPI Communication
  Pins 2-13 can be used for analog output via a Technique Called Pulse Width Modulation (PWM)

## Slide 14: Arduino Mega Pin Layout
The full detail pinout can be found at:
https://docs.arduino.cc/resources/pinouts/A000067-full-pinout.pdf

## Slide 15: Digital Output Applications
Driving an LED with I/O pin as a current source.
To use a pin as an output, the Arduino controls the voltage of the output
Driving an LED with I/O pin as a current sink.
HIGH pin turns LED on.
LOW pin turns LED off.
LOW pin turns LED on.
HIGH pin turns LED off.

## Slide 16: Output Pin as a Current Source
In this case, the pin supplies the current to the load
When a pin is HIGH, current flows from the pin through the load to GND
When a pin is LOW, no potential difference between the pin and GND, so no current flows
The Arduino can safely supply up to 40 mA
A current-limiting resistor may be needed in some applications to ensure the microcontroller is not damaged

## Slide 17: I/O Pin as a Current Sink
Sink in current sink refers to the pin’s ability to receive current
The current comes from some other source (External Power Supply, Arduino 5V pin)
When pin is LOW, current flows from the +5V power supply through the load into I/O pin
When the pin is HIGH, no potential difference between the pin and +5V, and no current flows
The Arduino can safely sink 40 mA, the same as the source limit
Again a current-limiting resistor may be needed in some applications to ensure the microcontroller is not damaged, especially if the external source is greater than 5V

## Slide 18: Input Pins
Digital Inputs are even simpler
The Arduino measures the voltage at the pin and returns a 1 for 5V and 0 for 0V
  Similar to a multimeter, in voltage mode, the input pin will have a high resistance, so very little current will flow when the pin is being read

## Slide 19: Floating Inputs
So what happens if you try and read a pin that is not connected to anything
  The unconnected pin is called “Floating”
The pin will be in an unpredictable HIGH or LOW state depending on small charge or discharge paths on the PCB, Radio Frequency noise, temperature effects, etc.
In most digital input applications, you want to remove the random effect and give a defined state by using a “Pull Up” or “Pull Down” resistor

## Slide 20: Pull Up/ Pull Down
Pull Up resistors:
Connect the I/O Pin to +5V to “pull up” the voltage to the 1 value when the input is idle
Connect the I/O Pin to 0V to “pull down” the voltage to the 0 value when the input is idle
Input
Signal
Input
Signal
Pull Down resistors:

## Slide 21: Basic Digital I/O Functions
We must set the pins as Input or Output
The digital pins on the Arduino Mega are set to input as default (since this high resistance it is the safe state)
To use digital pins we have 3 different functions
  pinMode(pin, mode) sets the pin as an input or output
    INPUT and OUTPUT are defined as variables so they can be used in mode
  digitalWrite(pin, value) is used set a pin to 5V or 0V
    HIGH and LOW are again defined variables so you can use them for value
  digitalRead(pin) reads the pin and returns either a 1 (for 5V) or a 0 (for 0V)
  For all, pin the number of the pin as labeled on the Arduino

## Slide 22: Configuring Pins Examples
Here is an example of setting pin 13 as an OUTPUT, and then “turns on” the pin for 1 second and then turns it off.
Notes: Arduino, Arduino. “PinMode().” Arduino - Introduction, 2018, www.arduino.cc/reference/en/language/functions/digital-io/pinmode/.