## Slide 1: System Design

## Slide 2: What is system design?
High-level design identifying the system processes, functional components, and their interfaces
Derived from system requirements
Provides an overview of the project
  Define the components that are needed
  Establish how components “communicate” with other components
  Determine how to modularize the project into discrete work packages
  Identify critical interfaces that must be well defined
Used to provide initial cost, schedule & resource estimates
Little or few implementation details
  As system design is refined, and lower-level subsystems are included, implementation issues may need to be addressed

## Slide 3: System design steps
Define project goal and objectives
Develop the project system requirements
Identify the major system components that satisfy the system requirements
Identify the major system interfaces
Refine the system design
  Define subsystems making up each component
  Specify interfaces between subsystems
Establish management controls for the system interfaces

## Slide 4: Traceability Matrix
Shows the relationship between requirements and the components that satisfy these requirements
  Commonly used in software engineering, but has application to hardware as well
  Used to ensure that the system design properly addresses the project needs and does not incorporate any unnecessary components
Format of the matrix can vary widely, but generally includes the following for each requirement
  Identification number
  Description of the requirement
  Description of the component that satisfies the requirement
  Description of proof that verifies a components or system satisfies the requirement

## Slide 5: Sample NASA Flight Mission Traceability Matrix

## Slide 6: System design steps
Define project goal and objectives
Develop the project system requirements
Identify the major system components that satisfy the system requirements (Initial System)
Identify the major system interfaces (Initial System)
Refine the system design
  Define subsystems making up each component
  Specify interfaces between subsystems
Establish management controls for the system interfaces

## Slide 7: Initial System Design
Development of the initial system design can, at times, go hand-in-hand with refinement of the system requirements
  Functions needed to satisfy the science requirements define the initial system
For example, to perform any payload will probably need these functions
  You will need a sensor (detector system)
  You will need to power the sensor (power system)
  You will need to read data from the sensor (data acquisition system)
  You will need to store the data (data archive system)
  You will need to control the sensor, readout, and storage (control system)
  You will need to analyze the data (ground data system)
As the design develops, you will determine specific detailed requirements for the above systems
  For example, the power system will need to supply volts & milliamps to the sensor, data acquisition, archive and control systems

## Slide 8: Major System Interfaces
An interface describes the linkage between major subsystems or processes
There are multiple types of interfaces
  Mechanical: How systems physically fit together
  Power: What voltage and current flows between the systems
  Electronic: The characteristics of electrical signals between systems
  Data: Format and content of information transferred between systems
  Thermal: How does heat flow between systems
  Software: How modules communicate with other modules or hardware
The type and characteristics of all interfaces need to be identified and defined

## Slide 9: System Level Drawing Example
High-level overview of a balloon platform that could carry eight Cubesat payloads
  Primary subsystems are identified (Power, CubeSats, FCU, etc.)
  Directionality and content of major interfaces are identified

## Slide 10: System design steps
Define project goal and objectives
Develop the project system requirements
Identify the major system components that satisfy the system requirements
Identify the major system interfaces
Refine the system design
  Define subsystems making up each component
  Specify interfaces between subsystems
Establish management controls for the system interfaces

## Slide 11: Refining the System Design
After the major systems and interfaces are identified, the subsystems are described
  The process is repeated for each of the subsystems (i.e. the boxes of the system diagram) defined in the top-level system design
For example, the Power Subsystem in the previous slide requires the following components
  A source that supplies the energy for the entire platform
  Separate supplies to convert the source power to the proper voltage and current required by the other systems (FCU, DAU, etc.)
Each of the subsystem interfaces is given a more detailed specification
  How many and what kind of interfaces do the subsystems need?
  What are the details (Voltage, current, logic levels, etc.) of the interface

## Slide 12: Subsystem Level Example
Subsystem design provides additional details
  Major functional components are identified and expressed
  Shows that system requirements are satisfied
  Most important interface details are revealed
Still little hardware or implementation dependence

## Slide 13: Moving to Component Specifics
The system design refinement process continues by specifying the major components of the subsystems
For example, the FCU supply in the power system might include the following major components
  A relay to turn the supply on / off by computer control
  A DC / DC converter to provide the required voltage from the source power
  An inline sensor so that volts and amps can be monitored in real-time by the computer
This is not a schematic drawing
  The type of component and ratings should be identified, but not specific parts
  I.E. You know you need a 5V/2A relay but not a specific part number

## Slide 14: Refined Subsystem Example
Implementation and hardware details are starting to appear
Interfaces are close to being fully defined
Next step would be full hardware and interface specification

## Slide 15: System design steps
Define project goal and objectives
Develop the project system requirements
Identify the major system components that satisfy the system requirements
Identify the major system interfaces
Refine the system design
  Define subsystems making up each component
  Specify interfaces between subsystems
Establish management controls for the system interfaces

## Slide 16: Controlling Interfaces
Interfaces between systems need to be defined
An ICD can be helpful during system design
  Written description of the interface that is modified only under specific, previously defined conditions and is used by team personnel for implementation
  Written specification of the interface
  Obtain agreement between stakeholders on the interface characteristics
Controlled ICDs should be used to help manage potential risks
  When an interface error or mismatch could result in project failure
  When stakeholders implementing the interface ends are separated in either geographic distance or time